## Slide 1
Welcome

## Slide 2
BEST PRACTICE UNDER IWMP BATCH-III
PATHANAPURAM BLOCK, KOLLAM

## Slide 3
STATE :KERALA
DISTRICT :KOLLAM BLOCK :PATHANAPURAM PROJECT :IWMP III PIA :BLOCK PANCHAYATH
PATHANAPURAM
WATERSHED :KADAKKAMON

## Slide 4
PRACTICE
40 household open wells in the draught affected locations of the watershed have been provided with devices for using roof water to recharge them

## Slide 5
Nearly 24075 families
inhabit the project area
There are only 17437
open wells in the project area
Most of these wells
get dried up during summer
(about 5-6 months)

## Slide 6
Affected families used to
deepen their wells every summer for getting water
instead of augmenting ground water recharge in the localities
They kept on wasting their hard earned money on thewasteful effort

## Slide 7
METHODOLOGY
The methodology adopted in the case is quite simple
The drainage from the rooftops is diverted by means of pipe lines to a recharge pit made near the well

## Slide 8
Lead line from the roof
Recharge pit
The well

## Slide 9
Rain water
from the roof tops has thus been used to recharge the wells.
Members from benefited families have been identified as the User Groups

## Slide 10
In most cases,
the house owners themselves had opened the pit
Many of them
belong to BPL category

## Slide 11
The House Owner Mr. M.B. Rameshan,
Renju Bhavanam, Punnala P.O,
Pathanapuram, Kollam Dist
opens a recharge pit by his well

## Slide 12
Slope direction

## Slide 13
A typical recharge pit upstream the well

## Slide 14
HOUSE OWNER:
PRAMEELA SURESH
AMMU NIVAS, PUNNALA(P.O)
PUNNALA,PATHANAPURAM,KOLLAM(DIST)
A recharge pit
covered with slab

## Slide 15
Another recharge pit

## Slide 16: It was on of the EPAs

## Slide 17: Rain water from about 4000 M2 of roof tops has been utilised by this The total quantity of rain water thus conserved amounts to about 9760 M3

## Slide 18
IMPACT
The intervention generated good impacts.
All the 40 families could quite immediately avail the benefit of the summer rains
The water level in the wells have recorded an average rise of 0.9 -1.4 m

## Slide 19
So also, the local ground water stock of the area has been substantially enhanced by the percolation envisaged
under the system as is evident
from the enhanced availability of water
from the sources downstream

## Slide 20
TIME SPAN
The activity
was completed in a period of
one month
And the result was immediate
for the lavish summer showers
in the area

## Slide 21
LEVEL
The practice was taken up
at the PIA level with the involvement and participation
of the benefited families

## Slide 22
RESOURCE
REQUIREMENTS
On an average, a sum of Rs 7,000/- has been spent per well for the purpose
Beneficiary contribution has been collected from the concerned family to augment the WDF

## Slide 23
Total expenditure involved
in the activity is about Rs. 2,96,000/-

## Slide 24
REPLICATION
UPSCALING
The practice can easily be replicated at household level as the technology is simple and the investment is meagre.
The project intents to further simplify the methodology by substituting the installation of pipe lines with simple and indigenous house yard management techniques .

## Slide 25
KNOWLEDGE TRANSFER
The practice has become a very effective and motivating tool to disseminate the message “recharge water sources to solve drinking water scarcity”.
The practice has been quite successful in demonstrating the effectiveness and sustainability of rain water harvesting

## Slide 26
SUSTAINABILITY
Most of the buildings in the Watershed area have got roof tops suitable for harvesting the rain water for recharging wells
The success of the practice will motivate the community to take up the activity in a comprehensive manner rendering it sustainable

## Slide 27
EXPOSURE VISITS
Stakeholders from other projects shall be given opportunity to familiarize with the methodology and to understand the advantages and impacts of it by arranging necessary exposure visits to the locality.
Students from various educational institutions, workers from MGNREGS etc, shall also be benefited by such visits.

## Slide 28
CERTAIN VIEWS

## Slide 29
recharge pit

## Slide 30
Pipe alignments
Tiled roof

## Slide 31
recharge pit

## Slide 32
Location of activity
Between 904’50” and 905’50” North Latitude
and 76053’2” and 76055’7” East Longitude

## Slide 33
THANK YOU